## Slide 1: System Architecture - Overview

## Slide 2: System Architecture - Requirements
Communication Protocol Support
  OCPP Protocol
  WebSocket Communication
Concurrent Tasks Scheduling(Multithreading + Coroutines)
  Coroutine Isolation
  Coroutines: Message Communication Management
  Coroutines + Thread: GUI Remote Interaction Interface
  Thread: Real-time Data Collection and Monitoring
  Thread: Execution of Charging Control Logic
System Scalability Design
  Support for Multi-Port Charging Management
  Data Storage and Analysis (Possibility of Providing Database Support)

## Slide 3: System Architecture - Implementation
OCPP v2.0.1 Message (JSON)
SetChargingProfileRequest {
"evseId": 1,
"chargingProfile": {
"id": 1,
"stackLevel": 1,
"chargingProfilePurpose": "TxProfile",
"chargingProfileKind": "Absolute",
"chargingSchedule": [{
"id": 1,
"chargingRateUnit": "W",
"chargingSchedulePeriod": [
{ "startPeriod": 0, "limit": 2845 },
{"startPeriod": 10, "limit": 2845 }, …
],
"startSchedule": "2025-04-28T15: 41: 53Z"}, … ],
…
},
"customData": { "vendorId": "001" }
}
Complex hierarchical nesting, difficult to learn structure
Frequent reference to the OCPP Standard is required when writing code
High probability of error, with significant debugging costs
Communication
Scalability
Concurrent Tasks

## Slide 4
OCPP Message Generator
OCPP_Message = GenSetChargingProfileRequest.generate(
evse_id=1,
charging_profile= GenSetChargingProfileRequest.get_charging_profile(*args),
custom_data=GenSetChargingProfileRequest. get_custom_data(*args)
)
Use different generation functions to generate each message part
IDE provides type hints and Docstring
Reduces the learning cost of the OCPP Standard documentation
Structure encapsulation significantly reduces the probability of errors
Unified standard improve team collaboration efficiency
V2.0.1 —> 128 v1.6 —>78
System Architecture - Implementation
Communication
Scalability
Concurrent Tasks

## Slide 5
Signal Class -- Decoupling
  Supports synchronous/asynchronous calls
  No need for fixed callback functions
  Facilitates testing, debugging
  and expansion
Communication
Scalability
Concurrent Tasks
Problem: Multiple modules, complex calls, high coupling
System Architecture - Implementation

## Slide 6
System Scalability
  Database Support: the foundation for data storage and analysis
  Support for Multiple Devices (EVSEs, Shellies): Flexible hardware integration
  Modular Architecture Design: Easy to combine and expand
  Multi-Platform GUI Control Support: Unified Control
System Architecture - Implementation
Communication
Scalability
Concurrent Tasks

## Slide 7
System Architecture – Charge Point

## Slide 8
System Architecture - Project